## Slide 1: FXS and FXO
FXS Foreign eXchange Subscriber
      Provides Battery to the loop
      Generates Ring Voltage on the loop
      Performs Battery Reversal for Call connections
      Performs Battery Denial to signal Disconnect
      Detects Flash Hook, DTMF, Off-Hook, On-Hook
      Standard PSTN Loop provides 48vdc
      Acts like CO Switch Port
FXO Foreign eXchange Office
      Signals Off hook by connecting the loop
      Signals On-hook
      Signals Hook Flash
      Generates DTMF Tones
      PBX Analog Trunk Port that connects to CO or a basic Phone

## Slide 2: Major FXS Features
FXS Features
    Loop Start Signaling
        No Ground Start Signaling
    Default ringing voltage is around 81vdc when set to default 600ohms. A impedance setting of (600ohms at 20Hz) will generate around 90vdc for key systems that require higher VDC.
    Provides Stutter Tone for VM indications and light signal for phones that support this feature
    Call waiting
    Flash Hook for N-Way Calling
    The FXS ports support 1 tip and ring pair, not 2. Additional wiring has to be designed for have the BiB work with multi-lines systems through 1 RJ-11 port
    Supports Generation of RFC2833 DTMF. In-band DTMF via RTP can also be configured as of 8.8.3.9 version for BIB

## Slide 3: FXS Major Features Continued
    Supports adjusting timing of DTMF tones (Default 200ms)
    Support CLID via Bell 202 Standard
      CLID Type II Support for Call Waiting
      CLID Privacy Support
      CLID Adjustments or Information Order, Field Length and Time zone that is daylight savings aware
    16ms of EC on 4500 and 4600 Systems,
      the EdgeMarc 250 supports 32ms of EC
      The add on 4570 and 4603 Supports 32ms of EC
      The 4608T4WDPoE add on supports 16ms of EC
    Adjustments of Disconnect Signal timing (CPC Timer)
    Termination Impedance Options (600ohms is default US)
    Inter-digit Timer adjustments
    The 4600 systems support 20 REN = meaning 20 phones can be connect to all 6 ports

## Slide 4: Ringing on FXS Ports
Ringing Cadence is ring for 2s, silent for 4s, ring for 2s, silent for 4s and so on
The BiB Supports adjusting the ring time. The default ring time is 40 seconds. 40s = around 8-10 rings.
Ringer Time can be extended with the following configuration added to the “/etc/config/sipua_defs.conf” file
      SIPUA_INCOMING_ANS_WAIT_DELAY=<time_in_sec>

## Slide 5: DTMF Features on FXS
The FXS Ports are RFC2833 Compliant for DTMF by default
DTMF standard is play each tone for 80-300ms and the FXS ports on the EM are configured for 200ms max
Configuration Options for DTMF are as Follow and are added or any edits are done in the “/etc/config/sipua_defs.conf” file
      SIPUA_DTMF_MAX_TIME=<time in milliseconds>
        Configured for 200ms as default
      SIPUA_DISABLE_RFC2833=<on/off>
      For PRI Lines, the file to edit is “/etc/config/sipua_pri_defs.conf”
        PRI_DTMF_MAX_TIME=<time_in_ms, 50-400>
        PRI_DTMF_MAX_VOLUME=<volume, 2-15>

## Slide 6: CLID Feature Set
Caller ID, CID and CLID are the terms used for the same function
Two Modes of CLID
    SDMF (older mode and Not Supported on BiB)
      Single Data Message Format
        Date Stamped with calling Number
    MDMF (Supported)
      Multiple Data Message Format
        Date, calling Number and Name
CLID starts 500ms after the 2nd Ring for incoming calls
CLID Type I and Type II for Call Waiting are supported
Several Configuration Sections for the FXS
CLID standard is Bell 202 modem (1200 bps frequency-shift keying, or FSK)
Depiction of Caller ID On the Line

## Slide 7: Configuration Options for CLID
If the Order of the CLID Information needs to change
      SIPUA_CID_FIELD_ORDER=date:name:number (default)
If the Length of the Name Field needs to change
      SIPUA_CID_MAX_NAME_LENGTH=1-20 (default = 12)
Of the Length of the Number Field Needs to Change
      SIPUA_CID MAX_DIGITS=1-12 (default = 10)
In some rare cases the CLID voltage needs to change, add this line to increase the voltage
      SIPUA_CID_TX_LEVEL=4163 (not set)
When inbound CLID needs to be disabled, set this line to “on”
      SIPUA_CLID_SEND_DISABLE=on/off (not set, default to off)

## Slide 8: Answer and Supervisory Disconnect BiB Features
We all know answering on FXO is going off hook
We all know hanging up on FXO is going back on hook
FXS Signals as well for call connect and call disconnect. This is critical in cases when calls are processed by a PBX and Key systems
FXS Signal for Call connect is “Battery Reversal”
FXS Signal for Call over is “Battery Denial” or End of “Battery Reversal”
“CPC Timer” on the EM Sets the “Advisory Disconnect” signal
    CPC Default Timer is set to 800ms

## Slide 9: More on Disconnections
TIME
Power
Phone A
Phone B
Phone A Calls PBX
PBX Forwards Call to remote Phone B
Phone B Hangs Up
System has to Signal Leg 2 Call has ended
1.
2.
3.
4.
FXS
FXO
FXS
FXO

## Slide 10: Inter-Digit Timer for FXS
Most folks are familiar with inter-digit timer and dial plans on Cisco GW and CCM.
The EM does not have dial peer plans like when XXX-XXX-XXXX number of digits are dialed, send the digits via SIP immediately
A dialing of “#” after the last digits would trigger the number to dial immediately on FXS.
The inter-digits feature is used for knowing when to send the call. For the AT&T configuration we set this to 2s. This means that once the FXS receives each digit, the SIPUA waits for an additional 2s for any other digits before sending a call to the network.
The number of digits does not matter, the inter-digit timer triggers after the 1st digit or 10th digit if more than 2s lapse before dialing another digit.
If a customer dials only 4 digits, and then the timer threshold of 2s is reached, the 4 digit is number is sent by the FXS/SIPUA to the IPBE with an INVITE for what may be a wrong or not finished number.
Inter-digit setting only effects dialing outbound and does not effect DTMF being dialed while in a call.
PRI signaling is different and is not effected by Inter-digit

## Slide 11: Gain Settings on SIPUA/FXS
Default setting is -4/-4 for TX/RX
-# TX means the voice being transmitted needs to be softer sound
+# TX means the voice being transmitted needs to be louder
-# RX means the voice being received is softer
+# RX means the voice being received is louder than needed
Changing gain can help offset echo if the echo is Near End Echo created between the FXS port and PBX system