## Slide 1: EdgeMarc CLI commands

## Slide 2: Notes on Software CLI (cont’d)
Linux based file system running on flash
Most of the file system is read only in user mode; this means that shell scripts can only be run under the guidance of EWN Systems Engineers or TAC Engineers
Bash shell is used when logged in – helpful
keeps command history and tab for complete commands similar to Cisco/Adtran
A good number of needed unix utilities are available but this is not a redhat system.
CLI is used mostly for config review, check and also troubleshooting
CLI can be used for making specific configuration changes, but not all configuration changes
During login session, history is kept of commands. History is lost when logging out
TACACS Login or Local username/password will be used

## Slide 3: EdgeMarc VOS Directory Structure Tour
/
/etc
/var
/bin
/dev
/home
/lib
/mnt
/proc
/sbin
/sys
/tmp
/usr
/config
/mand
/conf
/net
Configuration Files
Configuration Scripts
Network Info, NAT Table for Example
ALG Information Directory

## Slide 4: Important Directories and Files Cont.

## Slide 5: Important Directories and Files Cont.

## Slide 6: Viewing the Interface Configurations
6
Checking the IP addresses of the LAN and WAN ports
  # ifconfig
    eth0 Link encap:Ethernet HWaddr 54:39:68:01:23:0E
    inet addr:1.1.1.3 Bcast:1.1.1.255 Mask:255.255.255.0
    inet6 addr: fe80::5639:68ff:fe01:230e/64 Scope:Link
    UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
    RX packets:12393803 errors:0 dropped:0 overruns:0 frame:0
    TX packets:12463775 errors:0 dropped:0 overruns:0 carrier:0
    collisions:0 txqueuelen:1000
    Interrupt:16 Memory:f7d00000-f7d20000
    eth1 Link encap:Ethernet HWaddr 54:39:68:01:23:0F
    inet addr:12.183.130.141 Bcast:12.183.130.143 Mask:255.255.255.240
    inet6 addr: fe80::5639:68ff:fe01:230f/64 Scope:Link
    UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
    RX packets:21168739 errors:0 dropped:0 overruns:0 frame:0
    TX packets:20979794 errors:0 dropped:0 overruns:0 carrier:0
    collisions:0 txqueuelen:1000
    Interrupt:17 Memory:f7c00000-f7c20000
    eth2 Link encap:Ethernet HWaddr 54:39:68:01:23:10
    inet addr:10.128.1.141 Bcast:10.128.3.255 Mask:255.255.252.0
    inet6 addr: fe80::5639:68ff:fe01:2310/64 Scope:Link
    UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
    RX packets:4193948 errors:0 dropped:0 overruns:0 frame:0
    TX packets:926 errors:0 dropped:0 overruns:0 carrier:0
    collisions:0 txqueuelen:1000
    Interrupt:18 Memory:f7b00000-f7b20000
    lo Link encap:Local Loopback
    inet addr:127.0.0.1 Mask:255.0.0.0
    inet6 addr: ::1/128 Scope:Host
    UP LOOPBACK RUNNING MTU:16436 Metric:1
    RX packets:1654 errors:0 dropped:0 overruns:0 frame:0
    TX packets:1654 errors:0 dropped:0 overruns:0 carrier:0
    collisions:0 txqueuelen:0
Notes: 6

## Slide 7: Viewing DHCP Leases
7
Viewing the status of DHCP leases
  All times in this file are in UTC (GMT), not your local timezone.
  This is not a bug. There is no portable way to store leases in the local timezone.
  # cd /etc/config
  # more dhcpd.leases
  << dhcpd.leases >>
  lease 192.168.2.15 {
  starts 2 2008/10/14 06:48:18;
  ends 5 2008/10/17 06:48:18;
  hardware ethernet 00:a0:d1:d0:9b:01;
  uid 01:00:a0:d1:d0:9b:01;
  client-hostname "bill";
  }
  lease 192.168.2.12 {
  starts 1 2008/10/13 14:46:21;
  ends 4 2008/10/16 14:46:21;
  hardware ethernet 00:04:f2:19:ca:ec;
  }
  lease 192.168.2.11 {
  starts 1 2008/10/13 14:46:16;
  ends 4 2008/10/16 14:46:16;
  hardware ethernet 00:04:f2:18:54:97;
Notes: 7

## Slide 8: DHCP and NAT status
8
To see if the DHCP Server is running
  # ps –ef | grep dhcpd
  24309 root 640 S N /bin/dhcpd -q eth0.1 eth0.100 eth0.200
  25151 root 452 S N grep dhcp
  Verification of dynamic NAT (port/address)
  # netstat -nat
  Active Internet connections (servers and established)
  Proto Recv-Q Send-Q Local Address Foreign Address State
  tcp 0 0 192.168.2.252:1025 0.0.0.0:* LISTEN
  tcp 0 0 192.168.2.1:5060 0.0.0.0:* LISTEN
  tcp 0 0 99.148.27.5:5060 0.0.0.0:* LISTEN
  tcp 0 0 0.0.0.0:80 0.0.0.0:* LISTEN
  tcp 0 0 0.0.0.0:22 0.0.0.0:* LISTEN
  tcp 0 0 0.0.0.0:23 0.0.0.0:* LISTEN
  tcp 0 0 192.168.2.252:7001 0.0.0.0:* LISTEN
  tcp 0 0 192.168.2.252:7002 0.0.0.0:* LISTEN
  tcp 0 0 192.168.2.252:7003 0.0.0.0:* LISTEN
  tcp 0 138 99.148.27.5:23 135.89.202.138:62986 ESTABLISHED
Notes: 8

## Slide 9: ARP Commands
9
To see a complete listing of ARP filters, type
  # arp -h
The following filters can be applied:
# arp -a display (all) hosts in alternative (BSD) style
# arp -s --set set a new ARP entry
# arp -d --delete delete a specified entry
# arp -v --verbose be verbose
# arp -n --numeric don't resolve names
# arp -i --device specify network interface (e.g. eth0)
# arp -D --use-device read <hwaddr> from given device
# arp -A -p, --protocol specify protocol family
# arp -f --file read new entries from file or from /etc/ethers
To flush the entire ARP cache:
# ip -s -s neigh flush all
Notes: 9

## Slide 10
10
  # cd etc/config
  # cat sipclients.2
  * 192.168.2.252 1025 6304474938 uri=sip:6304474938@192.168.2.252:1025 ndm=0 user=6304474938 nat=0 trn=0 trp=0 blaport=5060
  * 192.168.2.16 5060 6304474942 uri=sip:6304474942@192.168.2.16:5060 ndm=0 user=6304474942 nat=0 trn=1 trp=0 blaport=5060
  * 192.168.2.11 5060 6304474941 uri=sip:6304474941@192.168.2.11:5060 ndm=0 user=6304474941 nat=0 trn=1 trp=0 suburi=sip:SD8ts86-meccfempfbv5t0sqkvm2p4ji24k6hvgi096hfq92fugh9jpfhi0o0ohg6ohg00ho120mqobp82plsffoaofndsnk4o4u7e066qv4e50000107@12.194.226.140:5060;att=HATTCENTREX-5cfhslaerassa;transport=udp subuser=SD8ts86-meccfempfbv5t0sqkvm2p4ji24k6hvgi096hfq92fugh9jpfhi0o0ohg6ohg00ho120mqobp82plsffoaofndsnk4o4u7e066qv4e50000107 blaport=5060
  * 192.168.2.14 5060 6304474938-81754940 uri=sip:6304474938@192.168.2.14:5060;user=phone;transport=udp ndm=0 user=6304474938 nat=0 trn=1 trp=0 blaport=5060
  * 192.168.2.12 5060 6304474944 uri=sip:6304474944@192.168.2.12:5060 ndm=0 user=6304474944 nat=0 trn=1 trp=0 blaport=5060
  * 192.168.2.252 1025 6304474943 uri=sip:6304474943@192.168.2.252:1025 ndm=0 user=6304474943 nat=0 trn=0 trp=0 blaport=5060
Viewing the SIP Clients list
Viewing the SIP clients table
Notes: 10

## Slide 11: Debugging… debugged
11
When troubleshooting a case, it is optimal to pursue the following debug scenarios:
Packet capture (tcpdump) using the ‘any’ interface flag
Output of “sys_report” command
FXS related issue: All of the above and the fxs debug
PRI related issue: All of the above and the PRI debug
Further debug might be required
  ALG/B2BUA logging
  Output of system-related commands
Notes: 11

## Slide 12: CLI Command Reference - VoIP
Command | Purpose
# mandctl log 0x9 / # mandctl log 0 | Turns on ALG debugging for VOIP issues / Turns off debugging; note, mand logs are not meant to be perpetual!
# sys_report | Outputs entire running configuration to text on screen
# cat /var/mand/calls | Displays active calls on system
# cat /var/mand/sipservers_status | Displays SIP Server status as reflected on Survivability GUI page - lost messages, received messages, processing state (Active, Idle, Unreachable)
# cat /var/mand/sipservers_data | Displays SIP server status as reflected on GUI (IP Address, Port, Priority)

## Slide 13: CLI Command Reference – System Troubleshooting
Command | Purpose
# ifconfig | Displays all configured interfaces
# ewntmsctl –d | Displays T1 status
# ping address ¦ name | icmp testing
# arp | Displays arp status / connected MAC addresses
# traceroute | Conducts icmp traceroute
# cat /proc/net/ip_conntrack ¦ wc –l | Displays count of all NAT’d connections
# cat /var/log/messages # cat /var/log/messages.old | Displays message file up to 32K Displays messages rotated after 32K
# cat /var/log/messages # cat /var/log/messages.old | Displays message file up to 32K Displays messages rotated after 32K

## Slide 14: CLI Command Reference – System Management
Command | Purpose
# cat /etc/version | Displays VOS version on system
# cat /etc/platform | Displays hardware type
# cat /var/ewn_model | Displays model of system
# ewn save filename.conf1 or .conf2 | Saves running configuration to a file that can be exported off of the system
# cfg_commit | Saves any configuration change made to the CLI to the static configuration
# config_network | Restarts network services
# cfg_restore | Restores system to Comcast default manufacturing configuration

## Slide 15: Additional Useful System Debugging command (sys_report) for TAC and capturing info
15
  ‘sys_report’ is a new command that provides useful debug output. Usage is: # sys_report
  This command combines automates certain scripts and output from a multitude of commands, and provides the following
  Hardware info (/etc/platform)
  Firmware Version info (/etc/version)
  Date/Time stamp
  memory info (/proc/meminfo)
  Process info (ps –ef)
  File System info (df)
  CPU info (top)
  Active/configured interface info (ifconfig)
  Routing table display (route)
  certain mand files (tinfo, xml_info)
  VPN info and logs
  Kernel and OS output info (dmesg)
  message log output (var/log/messages and var/log/messages.old)
  Running configuration (mandctl dbg replay = /var/replay.cfg)

## Slide 16: Intro to the packet capture function
16
Because the EdgeMarc acts as a passive network probe, it utilizes the native linux ‘tcpdump’ command to sniff traffic on all of it’s interfaces. This command allows the operator to passively monitor packet activity going through the interfaces
# tcpdump –i <interface>
where <interface> is eth0 for the LAN side, eth1 for the WAN side, hdlc0 for T1, etc. Refer to ‘ifconfig’ output to better suit your environment.
Other options for ‘tcpdump’:
  # tcpdump –h gives all the options available with flags
  this will filter out SSH traffic from the LAN and/or WAN trace by source or destination IP address
  # tcpdump –ni any –s 0 host xxx.xxx.xxx.xxx
  This is the best script to capture, as it does not truncate the output and is good for printing to a pcap file:
  # tcpdump –ni any –s 0 not port 22
  This capture grabs only the well known SIP signaling port:
  # tcpdump –ni any –s 0 port 5060
  This capture grabs SIP signaling and Survivability ports:
  # tcpdump –ni any –s 0 port 5060 and port 5050
  This capture grabs SIP signaling and DNS, useful troubleshooting call processing related issues:
  # tcpdump –ni any –s 0 port 5060 or port 53
Notes: 16

## Slide 17: Saving a packet capture to a viewable Wireshark file
17
The EdgeMarc has the ability to store packet captures locally on the system, for later FTP to view in Wireshark.
It is important to realize that there is a finite amount of storage space, no more than 16M, so you must exercise caution when running packet captures.
To create a temporary storage file on the EdgeMarc, take the following steps:
# mkdir /var/ramdisk
# mount -t tmpfs tmpfs -o size=8M /var/ramdisk
After you have created the temporary storage space (in volatile memory), then you can execute any variation of the tcpdump command and save the output to the ramdisk. Conduct this while replicating or tracking the issue/scenario:
# cd /var/ramdisk
# tcpdump -ni any -s 0 port 5060 or port 53 -w test.pcap
tcpdump: WARNING: Promiscuous mode not supported on the "any" device
tcpdump: listening on any
34 packets received by filter
Enter CTRL c to stop traces on each window
Notes: 17

## Slide 18: ALG/B2BUA diagnostics script
The more information on the scenario involved the better the framework is to troubleshoot
Basic SIP call control and RTP debug:
  # mandctl log 0x9 (covers most SIP call control and RTP issues)
  # mandctl log 0x1000009 (SIP + STATE + INFO, used primarily for HA/Stateful Failover debug)
  # mandctl log 0x05000009 (SIP + Survivability, used when debugging Remote to Local Mode operation)

## Slide 19: Debugging the mand (ALG/B2BUA) process
19
Solution Benefits
Secure, high quality voice
Connectivity made easy
Monitoring and troubleshooting
Reduced OpEx
The new command is:
  # mandctl log <level> [file_%TIME%.txt[size]]
  ‘level’ is the required logging level.
  ‘file’ if given is the main file to log to.
  ‘size’ if given, is the maximum size of the log file.
  %TIME, if given, provides a timestamp of the file
  Rules of Engagement:
  The rotation will keep one old file (file.old) so it is important to ensure that the ‘size’ is no more than half the available ramdisk space.
  For example, if you create an 8M ramdisk, you should not give a size larger than 4M, and to be safe, allow some extra space
  Numbers must be used, not abbreviations or suffixes, i.e., 3500000 instead of 4M, 500K, etc).

## Slide 20: Debugging the mand (ALG) process - application
20
  # mkdir /var/ramdisk
  # mount -t tmpfs tmpfs -o size=8M /var/ramdisk
  # mandctl log 0x9 /var/ramdisk/test_%TIME%.txt 5000000
  This command will create a text file of the mandlog output; additionally it writes useful ALG configuration parameters that will be used for analysis by Engineering
  Because mand logging is taxing, you must always disable mandlogging after you have captured the problem scenario
  # mandctl log 0

## Slide 21: Common Cisco to EdgeMarc Command Matrix
Cisco Command | Edgemarc Command
show service-module T1 s0/0/0 | Network stats in GUI or ewntmsctl -d
show service-module T1 s0/0/0 performance-statistics | Advanced page of stats in GUI or ewntmsctl -D 0
wr mem | /etc/conf/bin/cfg_commit
copy run start | ewn save <file name.conf1 or .conf2>
show version | GUI, System Page or cat /etc/version. Uptime can be obtained from GUI or uptime commad
show diag | cat /var/ewn_model or cat /etc/platform
show run | view file created by the ewn save command via the more command
 | mandctl dbg replay then retrieve file /var/replay.cfg
copy start run | ewn load <file name> followed by /etc/conf/bin/cfg_commit
show ip interface brief | ifconfig -a For built in switch ports, mii-tool, or use Network page of GUI
show log | more /var/log/messages
show clock | date
show arp | arp -a from CLI
show ip route | route or netstat -rvn from CLI
copy tftp flash (for upgrade purposes) | Use GUI Upgrade function or netflash –kiH (node manager ip) (image name)
copy run tftp | ewn upload <filename> <ip address>
show voice port sum | cat /var/mand/uaHookstate (FXS Ports) or cat /var/mand/calls (total active calls)
show diag | cat /var/ewn_model
show mem sum | cat /proc/meminfo
show proc cpu | top
show ip nat translations | cat /proc/net/ip_conntrack
show crypto iskmp ¦ ipsec sa | /etc/conf/ipsec/ipsec auto --status