## Slide 1: Module 5.0
EdgeView Service Control Center

## Slide 2: Module 5.0: Performance Objectives
Gain hands on experience with the operation of EdgeView Service Control Center.
Participate in the installation and configuration of EdgeView and Report Server. Working in small groups, attendees configure EdgeView to communicate with EdgeMarcs and third party nodes.
Gain experience with a wide range of EdgeView feature sets including basic EdgeMarc management, configuring status and notifications, applying templates, and conducting MOS & SIP Analysis troubleshooting.
Report Server hands on demonstration.

## Slide 3: Module 5.0: Hands On Labs
Lab 1: Exploring EdgeView CLI interface
Lab 2: EdgeView GUI Menu familiarization
Lab 3: EdgeView User Management Setup & Configuration
Lab 4: Configure HTTPS & Secure EdgeView
Lab 5: DB Backup & Working with Administrative Tools
Lab 6: Managing client EdgeMarc & nodes
Lab 8: Diagnostic Capture & Analysis
Lab 9: Conducting Active VoIP Test & MOS Analysis
Lab 10: Hands On familiarization with Report Server

## Slide 4: Module 5.0: Demos
Demo 1: Basic EdgeView & Report Server install & setup using CLI & YaST2
Demo 2: Sanity Check Menu
Demo 3: Overview of EdgeView capabilities
Using web based Icon Bar / GUI Pages
Viewing EdgeMarc Inventory by Tenant & Group
Launching an EdgeMarc GUI from within EdgeView
Demo 4: VoIP Analysis & SIP Call Flow Ladder Analysis
Demo 5: Report Server installation & configuration with EdgeView
Demo 6: Report Server overview of report capabilities

## Slide 5: Lesson 5.1: EdgeView & Network Edge Orchestration
Introduction to EdgeView
Concept of Network Edge Orchestration in context of EdgeView & EdgeMarc

## Slide 6: Lesson 5.1: EdgeView Service Control Center
EdgeView provides visibility to all voice and data traffic with real-time alerts/alarms for remote troubleshooting and management, fault isolation and reporting, and automated provisioning.
CONFIGURATION AND MANAGEMENT
MONITORING AND VISIBILITY
TROUBLESHOOTING
ANALYTICS
REPORTING AND KPIs
SERVICE PROVIDER NETWORK
EDGEVIEW
SERVICE CONTROL CENTER
EDGEWATER INTELLIGENT EDGE
Quality Monitoring Points

## Slide 7: Lesson 5.1: Configuration & Management
EdgeView offers a centralized view of IP Telephony deployments with a single server supporting 50K Intelligent Edges.
Using EdgeView’s API service providers can use their EMS to prepare templates. EdgeView stores ‘gold templates’ for each EdgeMarc Intelligent Edge under management.
EdgeView auto discovers new EdgeMarc Intelligent Edges. Stored configuration templates can be pushed to devices simplifying installation.
SERVICE PROVIDER NETWORK
EDGEVIEW
SERVICE CONTROL CENTER
EDGEWATER INTELLIGENT EDGE

## Slide 8: Lesson 5.1: Monitoring & Visibility
Every EdgeMarc Intelligent Edge calculates average MOS scores for each call leg every 10 seconds with no impact to device performance or call quality.
EdgeView Service Control Center provides highly configurable email alerts to report on Below Threshold Events, device health, configuration changes, and SIP server registration changes.
Below Threshold Events (e.g. MOS < x.x) are reported to EdgeView Service Control Center in real time with statistics to evaluate root cause of the event.

## Slide 9: Lesson 5.1: Troubleshooting & Diagnosis
At call conclusion, the EdgeMarc Intelligent Edged sends a full report to EdgeView with complete statistics to troubleshoot and isolate call issues (bad quality, dropped calls, etc.).
Using EdgeView’s API service providers can use their EMS to prepare templates. EdgeView stores ‘gold templates’ for each EdgeMarc under management.
EdgeView can remotely initiate test calls (EM to EM or EM to phone) for diagnostics without service interruption.
SERVICE PROVIDER NETWORK
EDGEVIEW
SERVICE CONTROL CENTER
EDGEWATER INTELLIGENT EDGE
Switch Issue?
WAN Issue?
Config Issue?
Phone Issue?
LAN Issue?

## Slide 10: Lesson 5.1: Post Call Troubleshooting Example
At the end of each call, EdgeMarc posts complete statistics for each call leg to the EdgeView database. Below MOS Threshold calls can be analyzed to pinpoint the root cause of the issue.
MOS per Call Leg
% of Call Degradation due to Lost Package
Lost Packets
Below Threshold Call
MOS Records from 8/5/15 08:35 to 8/5/15 09:30 with MOS below 4.5
Showing 6 Call Legs
Leg 2
Leg 1

## Slide 11: Lesson 5.1: Reporting & KPIs
All call statistics stored in EdgeView are accessible through a robust reporting and analytics tool. Service providers use EdgeView Reporting to establish performance KPIs, isolate potential problems and continuously improve service performance.
Chart: Intelligent Edges with Most Below Threshold Events (Past 24 Hours)
| SB-EM872 | MV-EM635 | PHL-EM81 | TMP-EM423
Event Count | 7 | 5 | 2 | 1
Chart: Intelligent Edges with Worst MOS (Past 24 Hours)
| MV-EM635 | PHL-EM81 | SB-EM872 | TMP-EM423
Event Count | 4.01 | 3.85 | 3.71 | 3.15

## Slide 12: Lesson 5.2: Installing EdgeView & Report Server
Planning the EdgeView network deployment & installation
Setting up the Virtual Machine environment
Accessing the CLI
Logging into EdgeView
Main GUI Menu overview & navigation
Licensing options with EdgeView

## Slide 13: Lesson 5.2: Installing EdgeView
Refer to EdgeView Service Control Center (EdgeView SCC) Installation Guide
Need to get virtual machine environment up and running
Install is then relatively straightforward
EdgeView runs on OpenSUSE 13.1 with a YaST based interface for basic configuration

## Slide 14: Lesson 5.3: Linking an EdgeMarc to EdgeView
3 Simple Steps
Setup the firewall
Configure SNMP and Syslogging
Synchronize the time source
EdgeMarc
EdgeView
Notes: Update the slides b/c running on newer software - Updated with Newer Screenshots
We will look at the 5 basic steps required to provision an EdgeMarc:
  Connecting to the Web GUI for the first time
  Setting up the local and wide area network interfaces.
    We will cover setting up VLANS
    We will cover configuring DHCP All though neither VLANS nor DHCP are required to provide VoIP service, they are commonly used and are covered here.
  Turn on the firewall to secure the local area network.
  Setup traffic shaping to ensure delivery of a business quality voice service
  Configure the Application Layer Gateway

## Slide 15: Lesson 5.3: Link to EdgeView - Firewall
The firewall MUST be enabled for EdgeView
SSH is used by EV for remote control
SNMP is used by EV for remote monitoring
Notes: A word about navigating this presentation.
The large red arrow to the left of the “Configuration Menu” indicates the item that was selected. The body to the right of the menu shows the page presented after the menu item was selected.
In this instance you will see this page after you select “Network” from the configuration menu.
Configuring the LAN and the WAN is rather self explanatory.
Please note that if you obtain a WAN IP address using DHCP any DNS servers you enter here will preempt the servers received from your ISP.
If you plan to use VLANS be sure to check the “enable VLAN support” box.

## Slide 16: Lesson 5.3: Link to EdgeView – Services Configuration
Enable SNMPv1. The Read-Only community string must match the SNMP password in EV
Enable MOS scoring and set the MOS threshold
Set the Hostname
I recommend using the Debug filter level
Enable Syslogging. and set your EV as the remote host
Notes: A word about navigating this presentation.
The large red arrow to the left of the “Configuration Menu” indicates the item that was selected. The body to the right of the menu shows the page presented after the menu item was selected.
In this instance you will see this page after you select “Network” from the configuration menu.
Configuring the LAN and the WAN is rather self explanatory.
Please note that if you obtain a WAN IP address using DHCP any DNS servers you enter here will preempt the servers received from your ISP.
If you plan to use VLANS be sure to check the “enable VLAN support” box.

## Slide 17: Lesson 5.3: Link to EdgeView – System Time
Enable the SNTP server. I recommend you use the same Server as the EV.
Notes: A word about navigating this presentation.
The large red arrow to the left of the “Configuration Menu” indicates the item that was selected. The body to the right of the menu shows the page presented after the menu item was selected.
In this instance you will see this page after you select “Network” from the configuration menu.
Configuring the LAN and the WAN is rather self explanatory.
Please note that if you obtain a WAN IP address using DHCP any DNS servers you enter here will preempt the servers received from your ISP.
If you plan to use VLANS be sure to check the “enable VLAN support” box.

## Slide 18: Lesson 5.4: EdgeView Common Functionality
Making Backups of Edgemarcs
Signaling Captures & MAND logging
Troubleshoot with Edgeview
Report Server Overview
New Edgeview Features for 14.1

## Slide 19: Lesson 5.4: Managing Backups - Archived Backups

## Slide 20: Managing Backups - Automatic Backups

## Slide 21: Lesson 5.4: Signaling Captures & MAND Logging
We recognize that not all problems are able to be recreated on-demand
  Intermittent, every third Wednesday in odd-numbered month problems are rare, but they do happen
Wouldn’t it be nice to perpetually capture all Signaling messages and have them automatically uploaded to your FTP server?
  Hostname and time-date stamped for easy retrieval

## Slide 22: Lesson 5.4: Signaling Capture – On Demand

## Slide 23: 5.4: Ladder Diagram
SIP MESSAGE 1 100.13.11.57:5060() -> 74.112.29.118:7281() UDP Frame 1 29/Feb/16 13:24:31.2705 TimeFromPreviousSipFrame=0.0000 TimeFromStart=0.0000 INVITE sip:8132992616@acme.cyberpbx.net:7281;user=phone SIP/2.0 Via: SIP/2.0/UDP 100.13.11.57:5060;branch=z9hG4bK528988079C8FD386 Record-Route: <sip:4083517294@100.13.11.57;lr> From: "4083517294" <sip:4083517294@acme.cyberpbx.net:7281>;tag=DC6A839D-4144BC34 To: <sip:8132992616@acme.cyberpbx.net:7281;user=phone> Call-ID: a087aae1-773e3108-dece52ab@172.250.0.150 CSeq: 1 INVITE Contact: <sip:4083517294@100.13.11.57:5060> User-agent: PolycomVVX-VVX_1500-UA/3.2.2.0481 Supported: 100rel Supported: replaces allow-events: talk allow-events: hold allow-events: conference Max-forwards: 70 Allow: INVITE, ACK, BYE, CANCEL, OPTIONS, INFO, MESSAGE, SUBSCRIBE, NOTIFY, PRACK, UPDATE, REFER Content-Type: application/sdp Accept-Language: en Content-Length: 688 v=0 o=- 1456781070 1456781070 IN IP4 100.13.11.57 s=Polycom IP Phone c=IN IP4 100.13.11.57 b=AS:256 t=0 0 a=sendrecv m=audio 16834 RTP/AVP 115 102 9 0 8 18 127 a=rtpmap:115 G7221/32000 a=fmtp:115 bitrate=48000 a=rtpmap:102 G7221/16000 a=fmtp:102 bitrate=32000 a=rtpmap:9 G722/8000 a=rtpmap:0 PCMU/8000 a=rtpmap:8 PCMA/8000 a=rtpmap:18 G729/8000 a=fmtp:18 annexb=no a=rtpmap:127 telephone-event/8000 m=video 16836 RTP/AVP 109 96 34 31 a=rtpmap:109 H264/90000 a=fmtp:109 profile-level-id=42800d a=rtpmap:96 H263-1998/90000 a=fmtp:96 CIF=1;QCIF=1;SQCIF=1;K=1;N=1 a=rtpmap:34 H263/90000 a=fmtp:34 CIF=1;QCIF=1;SQCIF=1 a=rtpmap:31 H261/90000 a=fmtp:31 CIF=1; QCIF=1

## Slide 24: Lesson 5.4: Troubleshoot with Edgeview
Using the EVA to perform group level actions
Using the EVA to monitor / maintain EdgeMarcs
Using the EVA to troubleshoot EdgeMarcs
Company Confidential

## Slide 25: Lesson 5.4: Perform group level management actions
1
EVA facilitates performance of group level administrative actions on a target classification of EMs
1: New group creation
2: Group level management
2

## Slide 26: Lesson 5.4: Perform group level management actions
EVA facilitates performance of group level administrative actions on a target classification of EMs
1: Perform group level script execution
2: Push licenses via CSV file input to group
3: Upgrade and reboot group
4: Create reachability rules
5: Move EdgeMarcs between groups or delete them from groups
2
1
3
4
5

## Slide 27: Lesson 5.4: monitor and maintain EdgeMarcs
1
Item 1: Exhibits the Softswitch/SBC reachability as per Survivability settings on EM
Item 2: Exhibits system health, number of successful calls since reboot, etc.
2

## Slide 28: Lesson 5.4: Password Management
Use this menu set to edit the passwords that the EVA will utilize for SSH, Web, SNMP, etc for an EM

## Slide 29: Lesson 5.4: EM Access Settings
Use this menu set to edit the passwords that the EVA will utilize for SSH, Web, SNMP, etc for an EM

## Slide 30: Lesson 5.4: Accessing an EdgeMarc GUI or SSH session
Launch EM GUI – select either GUI proxy (through the EVA) or launch a local (PC) GUI (Firewall dependent)
Start SSH on EM – access the SSH console of target EM through the EVA (proxy)

## Slide 31: Lesson 5.4: Upgrade EdgeMarc License Key
31
Use case: If an EM license needs to be upgraded from 5-15 calls, the operator can use this option to push a new license key

## Slide 32: Lesson 5.4: Rebooting EdgeMarcs
Handle with care!!! By invoking this function, the operator can reboot the target EM (after a “are you sure you want to do that” dialogue )

## Slide 33: Lesson 5.4: Load monitoring
33
In some cases, understanding the load on an interface can yield reasons as to why a customer might be complaining of voice quality or signaling issues

## Slide 34: Lesson 5.4: Sys_Report
34
  In any escalation case, there is a requirement to collect a “sys_report” which is a snapshot of an EdgeMarc’s health and “goings-on”. The EM CLI equivalent is: # sys_report
  This command combines automates certain scripts and output from a multitude of commands, and provides the following
  Hardware info (/etc/platform)
  Firmware Version info (/etc/version)
  Date/Time stamp
  memory info (/proc/meminfo)
  Process info (ps –ef)
  File System info (df)
  CPU info (top)
  Active/configured interface info (ifconfig)
  Routing table display (route)
  certain mand files (tinfo, xml_info)
  VPN info and logs
  Kernel and OS output info (dmesg)
  message log output (var/log/messages and var/log/messages.old)
  Running configuration (mandctl dbg replay = /var/replay.cfg)

## Slide 35: Lesson 5.4: Sys_Report
35
Under the Node “Operation”, select “Execute script on EdgeMarc Execute script

## Slide 36: Lesson 5.4: Sys Report
36
Select “sys_report” from the drop down menu

## Slide 37: Lesson 5.4: Sys Reports
37
1: Choose “sys_report” script
2: Choose “Execute Now”
1
2

## Slide 38: Lesson 5.4: Sys Reports
38
1: EVA provides script execution status
2: Output of “sys_report” script is available for copying
1
2

## Slide 39: Lesson 5.4: Sys Log
39
Select “syslog” from the drop down menu

## Slide 40: Lesson 5.3: Sys Log Report
40
1: EVA provides script execution status
2: EVA displays the syslog file from the target EM
1
2

## Slide 41: Lesson 5.4: Sys Log Display
41
EVA allows for another method to collect syslog records from either a group of EdgeMarcs or individual EdgeMarcs for trending analysis
1: Select “Syslog Disp.” from top navigation pane
2: Choose a filter (regex)
3: Choose either individual or group
4: Select to have the contents of the report output on screen or in a text report
5: Choose collection timeframes (new, already received, or both)
1
5
2
3
4

## Slide 42: Lesson 5.4: MOS Graphing
42
A graphical view of recent MOS scores; this can allow the operator to see a trend in call quality measurements, as opposed to raw measurements with detail data

## Slide 43: Using the EVA to troubleshoot EdgeMarcs - analyze call quality and signaling issues-
43
The “Analysis” tab and submenus allow the operator to perform MOS analysis and signaling captures from the EVA console, rather than from the EM console

## Slide 44: Lesson 5.4: MOS Call Analysis
44
EVA MOS analysis provides flexible parameters to gather and correlate data:
By a data/time range
By importing a pcap file
By viewing a near-term snapshot in time
Also provides a step-by-step troubleshooting method to ensure that the EVA can collect MOS data.

## Slide 45: Lesson 5.5: New Feaures in EV 14.1

## Slide 46: Lesson 5.5: New Features
Improve the EdgeView GUI: New icons, tables new look and feel.
Add footer to EdgeView

## Slide 47: New Features EdgeView 14.1.0
Auto populate buttons for signal captures
Add mandctl display to Signaling Analysis page: Added a dropdown to the Signaling Capture page “MAND Log Capture Parameters” content

## Slide 48: New Features EdgeView 14.1.0
Feature request to keep captures up to 14 days

## Slide 49: New Features EdgeView 14.1.0
Access web GUI of a remote phone behind an EdgeMarc via EVA

## Slide 50: New Features EdgeView 14.1.0
Alert to apply patches

## Slide 51: New Features EdgeView 14.1.0
What is the recommended way to define an EdgeMarc with WLR (2 WAN links) in the EV?
  EdgeView detects EM Wan Link Redundancy failover now (as good as EdgeView can)
Need a way to simplify the editing of Device Templates

## Slide 52: New Features EdgeView 14.1.0
SCP support for Back up and Restore of the EVA data base.
  EV Database Backups can now be offloaded with SCP.

## Slide 53: New Features EdgeView 14.1.0
Productize AutomaticTrigger Diagnostics shown at Broadsoft Connections
  Live demo

## Slide 54: Improvements EdgeView 14.1.0
Performance improvements
    Replace perl DBI 'prepare' with 'prepare_cached' in perl scripts
  MOS record processing improvements (was done also for 14.0.1.patch4)

## Slide 55: New Features Report Server 14.1.0
RS: Need disk space check for Report Server
RS: Alert when MySql replication is broken