## Slide 1: Edgewater Training
Edgewater Certified Solutions Professional
Course 201: –Install & Secure EdgeMarc with EdgeView Service Control Center

## Slide 2: Course Logistics
Class times: 9:00 AM – 4:30 PM
Location details
Emergency Procedures
Planned breaks throughout the day
Class & exam accommodations
Instructor Contact information

## Slide 3: Course Overview
Module 1.0 Overview of Edgewater Networks Product Line & Network Edge Orchestration
Module 2.0 EdgeMarc Installation & Core Configuration
Module 3.0 EdgeMarc Configurations with IP PBX & Hosted VoIP
Module 4.0 Advanced Topics - Scripted Configurations
Module 5.0 Troubleshooting & Support Exercise

## Slide 4: Module 1.0
Overview of Edgewater Networks Product Line & Network Edge Orchestration

## Slide 5: Module 1.0: Performance Objectives
Acquire an understanding of EWN product line and explore LAN / WAN deployments.
Gain an awareness of EdgeMarc, EdgeView, and the concept of Network Edge Orchestration.
Participate in classroom lab configuration familiarization.
Develop Hands on experience with the Wireshark protocol analyzer.

## Slide 6: Module 1.0: Hands On Labs
Lab 1: Product familiarization
Lab 2: Planning VoIP Deployment & Setup
Lab 3: Classroom Lab Overview & Familiarization
Lab 4: Capturing Network traffic with Wireshark

## Slide 7: Module 1.0: Lessons
Lesson 1.1: Introduction to Company history and product line
Lesson 1.2: Overview of EdgeMarc Capabilities
Lesson 1.3: Introduction to EdgeView Service Control Center
Lesson 1.5: VoIP Core Concepts

## Slide 8: Lesson 1.1: Introduction to Company history and product line
  Overview of the EWN Product Line & History
  The value of EdgeMarcs & EdgeView as an integral part of every client architecture

## Slide 9: Lesson 1.1: Overview of EWN Product Line & History
founded in October 2002
San Jose, California, USA
Network Edge Orchestration
delivering real-time security, service quality optimization and analytics
UC focused
Service Providers, Over The Top, Hosted PBX, UCaaS, SIP Trunk
over 500k ESBCs deployed
looking after 20M Endpoints
US market leader
50% YoY growth, IHS Infonetics Q3 2015 No#1 ESBC vendor
Europe now!
GB, PL, NL, DE, AT, CH, IE and more soon to come!
Notes: Founded in 2002 in San Jose, California (heart of Silicon Valley). Currently the company core team is over 150 people and growing.
Always Voip/UC focused, working closely to our Customers, listening to their needs. Our speciality are IP-IP ESBCs running on Customer Network Edge
Which after over a decade of hard work crystalized as NEO – our solution and methodology towards deploying IP voice services
About NEO later on
There is one value that proves our message and Customer approach being mature – 500k deployed ESBC, which handle voice services towards over 20M endpoints like IP Phones and IPPBXes
Those devices are deployed across most of the significant Service Provider in the US, most recognizable brands being: AT&T, Comcast, Cablevision, COX
This accomplishment was recognized by IHS Infonetics pointing EWN as No#1 ESBC vendor in US for Q3 2015.
Currently we are on the path to replicate this success in Europe, so you can be sure to hear about us quite often in the future.

## Slide 10: Lesson 1.1: Overview of EWN Product Line & History
  Deep domain expertise & support capabilities for Voice & Video Over IP
  Customer premise “Edge” devices at every location providing advanced LAN/WAN ingress-egress security & control for network traffic:
    EdgeMarc
    EdgeProtect
  Cloud / Service Provider based EdgeView Service Control Center
    EdgeView Server
    Report Server

## Slide 11: Lesson 1.1: Overview of EdgeMarc
WAN
IP PBX / SIP Server
PSTN
PSTN Gateway
PRI

## Slide 12: Lesson 1.1 Overview of EdgeView Service Control Center
WAN
EdgeView Server
San Diego
Chicago
Tampa
Report Server

## Slide 13: Lesson 1.1: Overview of EWN EdgeMarc Product Line & History
WAN
Calls
2
50
1,000
2,000
15
455x/457x
7301
Ethernet
Quad T1/E1
FXS/FXO
250AE
Ethernet
ADSL 2/2+
FXS/FXO
10
4601
Ethernet
Quad T1/E1
Dual PRI
4550/4552
4570/4571
10/100/1000
Ethernet
Dual WAN
4750
10/100/1000
Ethernet
Dual WAN
100
Large Office
Medium
SoHo
Small
4601
4750
Mbps
7400

## Slide 14: Lesson 1.1: EdgeMarc Product Line

## Slide 15: Lesson 1.1: Review
Edgewater Networks founded in 2002. Deep domain expertise in VoIP deployment, optimization & security.
EdgeMarc product line provides a wide range of essential functions that ensure clients converged voice & data LAN / WAN infrastructure is secured, reliable, and efficient.
EdgeView Service Control Center provides service providers and large multi-location clients with extraordinary control and management of complete EdgeMarc and VoIP infrastructure.

## Slide 16: Lesson 1.2: Deploying EdgeMarcs - EdgeMarc 4700

## Slide 17: Lesson 1.2: Deploying EdgeMarcs
  What can an EdgeMarc actually do?
  Overview of EdgeMarc capabilities including:
    Firewall / NAT
    Application Layer Gateway
    B2BUA defined
    WAN High Availability & Survivability
    Traffic shaping & management
    Monitoring
    Specialized VoIP capabilities
  Common VoIP LAN infrastructure, Enterprise Edge, Hosted VoIP
    IP PBX, PSTN Gateways, IP Phones, SIP Trunking
  Security considerations and the role of the SBC
  EdgeMarc with existing Firewall
  Hosted VoIP – Reliability considerations & options for securing hosted VoIP

## Slide 18: Lesson 1.2: Deploying EdgeMarc - 4700 Physical Interfaces
RS232 Interface
2 Ethernet WAN Ports
8 Ethernet LAN/VLAN Ports
Reset Button
SD Card Slot

## Slide 19: Lesson 1.2: Deploying EdgeMarc - What can an EdgeMarc do?
EdgeMarc provides customers with a LAN/WAN integration device with a wide range of essential network functions.
Along with all the core LAN/WAN edge functionality that you would expect such as NAT traversal, VLAN support (both LAN & WAN sides), EdgeMarc offers a host of advanced functions:
  Extensive VoIP support capabilities
  Very advanced and easy to deploy DHCP Server
  Sophisticated WAN & VoIP redundancy & Survivability features
  Traffic Prioritization & Traffic Shaping capabilities that support VoIP deployment
  Firewall Traversal and pairing arrangements that support built in VoIP ALG – Application Layer Gateway

## Slide 20: Lesson 1.2: Deploying EdgeMarc - Capabilities
The EdgeMarc provides client VoIP deployments with:
A voice, video and data firewall
A router
  VLAN
  DHCP Server
  VPN Tunnels
  WAN Link Redundancy
Traffic management and prioritization tool
  (Application Layer Gateway –ALG)
  Call quality monitoring (MOS Scoring)
Troubleshooting tool
VoIP B2BUA – Back to Back User Agent with survivability features
An EdgeMarc connects and simplifies Business VoIP and Data networks
*
Notes: *

## Slide 21: Lesson 1.2: Deploying EdgeMarc - Capabilities
POTS
4xT-1
SIP Trunk
Ethernet
Analog
Phone
Fax
Legacy
PBX
IP
PBX
IP Phone
Network Devices
DSL
VPN
LAN Side
WAN Side
EdgeView
EdgeMarc = Single Box for Connectivity, Quality and Management

## Slide 22: Lesson 1.2: Deploying EdgeMarc - Common VoIP Infrastructure
WAN
IP PBX / SIP Server
PSTN
PSTN Gateway
PRI

## Slide 23: Lesson 1.2: Deploying EdgeMarc - with existing Firewall
EdgeMarc can act as a Firewall OR work in parallel with a client’s existing Firewall
When working in parallel, the EdgeMarc can provide VoIP specific security using:
  its sophisticated built in VoIP-ALG “Application Layer Gateway”
  Act as a B2BUA – Back to Back User Agent for all VoIP traffic

## Slide 24: Lesson 1.2: Deploying EdgeMarc - Security considerations
EdgeMarc capabilities allow it to act as a “Session Border Controller”, isolating VoIP traffic and providing a “Demarcation” point that Service Providers can easily monitor with EdgeView
Isolating VoIP equipment “behind” a device that can monitor incoming / outgoing VoIP traffic is critical

## Slide 25: Lesson 1.2: Deploying EdgeMarc - Hosted VoIP
The Hosted VoIP market is growing at a very rapid rate
Clients connect their VoIP Phones third party that provides the “IP PBX” features & connectivity to the legacy PSTN
May be offered by a Service Provider on their WAN network or “Over The Top” by any third party provider using The Internet
EdgeMarc is a perfect “demarcation point” that can protect client VoIP equipment

## Slide 26: Lesson 1.2: Deploying EdgeMarc - Review
EdgeMarc is “Little Box that Could”
EdgeMarc feature set is ideal for client VoIP networks that span multiple locations and require sophisticated support for:
  Legacy Equipment
  Management & remote monitoring
  Advanced VoIP Security

## Slide 27: Lesson 1.2: Deploying EdgeMarc - Questions
What is a Firewall?
What is a Session Border Controller, how does it differ from a Firewall?
What is the difference between SBC and
  VoIP ALG
  B2BUA
Can the EdgeMarc act as a:
  Firewall
  SBC
  VoIP ALG
  B2BUA

## Slide 28: Lesson 1.2: Deploying Edgemarc - Network considerations
  From a single device to a multi-location client
  Supporting Servers & VoIP endpoints in typical EdgeMarc VoIP deployments
  IP PBX: LAN or WAN based?
  Introduction to core deployment concepts

## Slide 29: Lesson 1.2: Deploying Edgemarc - multi-location client
Client VoIP infrastructure grows in complexity as they:
  Add locations
  Acquire companies with legacy PBX infrastructure, multi-vendor VoIP equipment with differing SIP signaling requirements
  Provide voice service for offsite / home based workers
  Grow internationally – multi codec support, ISDN PRI, etc
EdgeMarc can provide an onsite integration that supports all these diverse deployment scenarios
EdgeView can provider a control plane to support deployment, management & monitoring of VoIP infrastructure.

## Slide 30: Lesson 1.2: Deploying Edgemarc - Multi-Location Business
WAN
IP PBX / SIP Server
San Diego
Chicago
Tampa

## Slide 31: Lesson 1.2: Deploying Edgemarc - Support Servers & endpoints
EdgeMarc works with existing client VoIP infrastructure:
  IP PBX
  IP Phones
  PSTN Gateways
  SIP Trunking Service Providers
  Support Servers such as
    FTP Provisioning Server
    DHCP Server
    DNS Server

## Slide 32: Lesson 1.2: Deploying Edgemarc - IP PBX: LAN or WAN based?
With single client locations it is common to have an IP PBX deployed in the LAN
As companies grow, they begin to explore the feasibility of migrating to a centralized IP PBX in the WAN
EdgeMarc & EdgeView can support both approaches

## Slide 33: Lesson 1.2: Deploying Edgemarc - IP PBX: LAN or WAN based?
WAN
IP PBX / SIP Server
PSTN
PSTN Gateway
PRI

## Slide 34: Lesson 1.2: Deploying Edgemarc - IP PBX: LAN or WAN based?
WAN
IP PBX / SIP Server

## Slide 35: Lesson 1.2: Deploying Edgemarc - core deployment concepts
VLAN considerations in VoIP deployments
DHCP Server vs DHCP Relay – What do you need in your deployment?
Advantages of built in EdgeMarc DHCP server in VoIP LAN configuration
Phone provisioning Servers – FTP, HTTP, TFTP
DNS Servers – The role of the DNS SRV record in finding SIP Servers

## Slide 36: Lesson 1.2: Deploying Edgemarc - core deployment concepts
VLAN considerations in VoIP deployments
VLAN – “Virtual LAN” is a very well established Ethernet standard
Original idea evolved as larger and larger Ethernet switches were deployed.
Provide a level of “isolation” between Ethernet devices connected to the same Ethernet switch / inter-connected switches
IP Phones, IP PBX, PSTN Gateways can all be assigned to their own “VLAN”, helping isolate VoIP devices from all the other LAN equipment such as PCs, servers, printers, etc

## Slide 37: Lesson 1.2: Deploying Edgemarc - core deployment concepts
DHCP Server vs DHCP Relay – What do you need in your deployment?
Dynamic Host Configuration Protocol Server
  Centralize the provisioning of IP Addresses for all devices
  Can have a DHCP server on each LAN or one central WAN based DHCP server
EdgeMarc supports both approaches
  Act as a DHCP Server for the LAN & DHCP client on WAN
  Act as a “DHCP Relay” for all LAN devices, connecting to a centralized WAN based DHCP server

## Slide 38: Lesson 1.2: Deploying Edgemarc - EdgeMarc as DHCP Server
WAN
LAN Devices send out DHCP Discover Packets to 255.255.255.255
EdgeMarc DHCP Server responds with Options

## Slide 39: Lesson 1.2: Deploying Edgemarc - EdgeMarc as DHCP Relay
WAN
DHCP Server
EdgeMarc as DHCP Relay

## Slide 40: Lesson 1.2: Deploying Edgemarc - EdgeMarc as DHCP Relay
WAN
DHCP Server
LAN Devices send out DHCP Discover Packets to 255.255.255.255
DHCP Discover Forwarded

## Slide 41: Lesson 1.2: Deploying Edgemarc - Phone Provisioning Servers
IP “endpoints” can be manually configured or their configuration settings can be centralized managed
Typically IP Phones need to obtain:
  IP Address details from a DHCP Server
  Learn the location of a Provisioning Server – TFP or FTP
  Learn the location of the IP PBX
EdgeMarc can provide IP Phones with all these details using the built in DHCP server and can even act as a provisioning server

## Slide 42: Lesson 1.2: Deploying Edgemarc - Phone Provisioning Servers
WAN
FTP Provisioning Server
DHCP Server
IP PBX / SIP Server
DNS Server

## Slide 43: Lesson 1.2: Deploying Edgemarc - Multi-LAN deployment
WAN
FTP Provisioning Server
DHCP Server
IP PBX / SIP Server
DNS Server
San Diego
Chicago
Tampa

## Slide 44: Lesson 1.2: Deploying Edgemarc - Review
EdgeMarc provides the “glue” that allows clients to grow multi-location VoIP infrastructure
EdgeMarc’s flexible features allow it to function as several critical VoIP support servers such as DHCP & FTP Provisioning, or work with external servers to support LAN VoIP devices

## Slide 45: Lesson 1.2: Deploying Edgemarc - Questions
Can you deploy IP Phones “without” using a TFP or FTP provisioning server?
What is the difference between a DCHP Server and DHCP Relay?
Can EdgeMarc act as a DHCP Relay?
Can EdgeMarc as a DHCP Relay AND a DHCP Server at the same time? Why/Why not?

## Slide 46: Lesson 1.3: Introduction to EdgeView Service Control Center
  Overview of Network Edge Orchestration
  What can you do with EdgeView?
  Managing EMs & other VoIP devices
  Analytics & Troubleshooting capabilities
  Typical deployment models

## Slide 47: Lesson 1.3: EdgeView Introduction
Centralized server to manage every aspect of dispersed EdgeMarcs & their associated VoIP servers / end points

## Slide 48: Lesson 1.3: EdgeView Capabilities
EdgeView is an Element Management System enabling:
EdgeMarc, EdgeConnect and IP phone management
  Backup and push configuration, upgrade for one or a population
Visibility to all voice and data traffic
MOS LAN side and WAN side analysis
Real-time alerts/notifications
Remote troubleshooting
Fault isolation and reporting
Automated provisioning
  IP phones with Plug & Dial
  EdgeMarc & EdgeConnect
  Inter multisite VPN
Notes: *

## Slide 49: Lesson 1.3: EdgeView Deployment Model
Cloud / WAN based deployment
One centralized server able to communicate with many EdgeMarcs
Can manage / monitor EdgeMarcs & their local VoIP Equipment
WAN
EdgeView Server
San Diego
Chicago
Tampa

## Slide 50: Lesson 1.3: EdgeView Review
EdgeView Service Control Center offers Service Providers & large enterprise clients with the ability to monitor and manage all deployed EdgeMarcs and associated VoIP Equipment
EdgeView Server and Report Server now deployed as Virtual Machines

## Slide 51: Lesson 1.3: EdgeView Questions
Is EdgeView Service Control Center typically deployed in each client LAN?
What is MOS?
Can EdgeView provide Backup and Restore capability to all associated EdgeMarcs? Bonus question – Does EdgeMarc have its own backup feature? Which is “better”?

## Slide 52: Lesson 1.4: Product Manuals & Knowledge Base
Open & review electronic copies of EM & EV manuals
Access EWN Knowledge Base & search for product manuals
Introduction to Edgewater technical support services

## Slide 53: Lesson 1.4: Open & review electronic copies of EM & EV manuals
All EdgeMarc devices use Edgewater “VOS” Voice Operating System
Review the EM 4700 hardware installation manual
Review the VOS 14.x manuals

## Slide 54: Lesson 1.4: Access EWN Knowledge Base
Visit https://edgwaternetworks.com/kb
Edgewater maintains an excellent free Knowledge base site where you can find copies of all the latest product manuals and many helpful articles
Docs stored in pdf format, can be downloaded
Fully searchable

## Slide 55: Lesson 1.4: Edgewater technical support services
The Edgewater TAC support group focuses on resolving the interruption of voice services to your end users
The Edgewater System Engineering group supports you in your pre sales and lab certification activities

## Slide 56: Lesson 1.4: Technical Support – Gather Information
A summary of the environment.
A precise statement of the symptom(s) you are experiencing.
The steps you have already taken to troubleshoot the issue.
The steps required to duplicate the issue.
A sys_report from the affected box.
Capture SIP signaling in a PCAP if necessary. We will cover these tasks later.
A precise statement of what you are asking support to help you with.
Page 56
Notes: Update the slides b/c running on newer software - Updated with Newer Screenshots
We will look at the 5 basic steps required to provision an EdgeMarc:
  Connecting to the Web GUI for the first time
  Setting up the local and wide area network interfaces.
    We will cover setting up VLANS
    We will cover configuring DHCP All though neither VLANS nor DHCP are required to provide VoIP service, they are commonly used and are covered here.
  Turn on the firewall to secure the local area network.
  Setup traffic shaping to ensure delivery of a business quality voice service
  Configure the Application Layer Gateway

## Slide 57: Lesson 1.4: Review
Edgewater knowledge base is easily accessible and searchable.
Edgewater technical support services are here to help.
Gather up as much information as possible before contacting Edgewater Tech Support

## Slide 58: Lesson 1.4: Questions
Search the Edgewater Networks knowledge base for the latest VOS manuals for the EM 4700.

## Slide 59: Lesson 1.5: Classroom Lab Configuration
The classroom lab is built using EM 4700 devices
Each group will run and control their own EdgeView Server
IP Phones may be provisioned manually, or using an FTP Provisioning Server
Asterisk IP PBX Servers are deployed for each group as either:
  LAN based IP PBX
  WAN based IP PBX

## Slide 60: Lesson 1.5: Classroom - IP PBX LAN Side

## Slide 61: Module 1.0: Review
Edgewater Networks is a technology leader in large scale, distributed VoIP deployments
EdgeMarc provides a robust feature set that allows clients to:
  connect legacy equipment to their VoIP network
  Secure VoIP infrastructure
  Manage and monitor all aspects of their VoIP network
VoIP standards allow multi-vendor equipment to operate together to provide “Full Duplex, Real Time” communications.

## Slide 62: Module 1.0: Quiz
What year was Edgewater founded?
What model of EdgeMarc are we using in the classroom?
Can the EM 4700 support connectivity to a legacy PBX via an ISDN interface?
How do IP Phones connect at Layer 2?
Can EdgeView provide Backup & Restore capability for registered EdgeMarcs?
What is SIP. What standards body is responsible for SIP?
Can SIP be transported over TLS?