## Slide 1: Module 2.0
EdgeMarc LAN/WAN Installation and Setup

## Slide 2: Module 2.0: Performance Objectives
Develop practical onsite EdgeMarc installation and core configuration skills.
Installers practice following configuration processes and securing EdgeMarc.

## Slide 3: Module 2.0: Hands On Labs
Lab 1: Accessing EdgeMarc CLI & GUI
Lab 2: Hands On EdgeMarc Basics: Firmware Upgrades, Backup & Restore, Time Settings
Lab 3: EdgeMarc LAN & WAN configuration
Lab 4: Securing EdgeMarc

## Slide 4: Module 2.0: Lessons
Lesson 1.0: Edgemarc Overview
Lesson 2.0: Basic Configuration
Lesson 3.0: Securing Edgemarc

## Slide 5: Lesson 2.1: EdgeMarc Physical Interface Options
View & identify EM LAN/WAN & PSTN interface options on various models including 4700, 4808, 4552, others.
Identify power supply requirements, grounding, password reset / default configuration button.
Understand the usage of SD card slot, console, & USB interfaces on various EdgeMarcs
Setting up an EdgeMarc, physical deployment considerations

## Slide 6: Lesson 2.1: EM LAN/WAN & PSTN interface options
Let’s explore the EM 4808 physical Interfaces
Working as a group, identify each physical interface
How could you use the 4808 to provide VoIP service to a legacy Nortel Norstar ISDN PRI capable PBX?
What is an Amphenol Connector?

## Slide 7: Lesson 2.1: Power, Grounding, Password / Default Config Reset
Review the hardware installation manuals to determine power requirements for your EM 4700
To reset the EM to default configuration, press the erase button three times in quick succession

## Slide 8: Lesson 2.1: SD card slot, console, & USB interfaces
The SD Card slot can be used to add additional memory storage to the EdgeMarc
Note that there is a performance hit. SD Cards should not be left in the EM
The USB interfaces are no longer included on EdgeMarc

## Slide 9: Lesson 2.1: SD card slot, console, & USB interfaces
The console Port is used to connect an RS232 serial cable
Allows CLI - command line access to EdgeMarc “VOS”
Embedded Linux built on Busybox distro
CLI access is also available via SSH

## Slide 10: Lesson 2.1: EdgeMarc, physical deployment considerations
Refer to the hardware installation manual.
EM 48xx is a 19 inch rack mounted deployment
EM 4700 may be desktop device, side connecting manuals are included to adapt for 19 inch rack mount

## Slide 11: Lesson 2.1: Review
EdgeMarc physical interfaces differ by unit
Some such as the 4808 include legacy PSTN interfaces such as T-1, ISDN PRI, and Analog FXO/FXS ports.
  FXS – Station Port
  FXO – Central Office Port

## Slide 12: Lesson 2.1: Questions
Does the EM 4700 support USB interfaces?
Does your laptop have an RS-232 interface?
  If not, how are you going to connect it to an EdgeMarc?
Can you connect a legacy PBX to an EdgeMarc and have the EdgeMarc act as a gateway between a PSTN standard and VoIP? How, explain?

## Slide 13: Lesson 2.2: Initial Configuration
Introduction to the EdgeMarc Voice Operating System
Understanding the EdgeMarc default LAN configuration settings
GUI vs Command Line Interface
Understanding basic Admin GUI functions

## Slide 14: Lesson 2.2: Initial Configuration - Voice Operating System
EdgeMarc VOS is Edgewater’s core software driving all EdgeMarcs
Built on “busybox” embedded Linux distro
Because you will have CLI root access it is possible for you to start manipulating the OS by adding or removing services, etc.
Don’t do that… Not a good plan 
Still, you can navigate the OS using typical Linux commands. Busybox, like most embedded linux distros supports a very limited set of Linux commands

## Slide 15: Lesson 2.2: Initial Configuration - LAN configuration settings
Start planning your EdgeMarc LAN deployment requirements
Determine DHCP requirements
DNS requirements
VLAN requirements (LAN and WAN Side)
VoIP Support requirements

## Slide 16: Lesson 2.2: Initial Configuration - GUI vs Command Line Interface
  There are three fundamental ways to access the EdgeMarc for configuration related settings:
    The Web Based GUI. Available at the EM default LAN IP and, if permitted in the Firewall, the WAN based IP, using either HTTP or HTTPS
    Accessing the GUI from a web browser as root can be done from the LAN side after the EM boots up
  CLI access from the console port using an RS232 cable
  SSH Access from LAN or WAN side after Firewall settings configured
  The default root user has two passwords:
    Root GUI default password is “default”
    Root CLI default password is “(Press & Hold the Shift Key)2345678109”

## Slide 17: Lesson 2.2: Initial Configuration - Basic Admin GUI functions
  In the hands on lab we will explore basic admin functions of the EdgeMarc:
  View License Key
  Encryption Key
  Backup & Restore
    Used to create and download a single backup of the individual EM. With EdgeView, this feature can be centralized in the EV server for all EdgeMarcs
  Firmware Upgrade
    Can access EM FTP server, or setup your own FTP server to control which VOS upgrades are available to the EdgeMarc. Like Backups, this can be managed globally in EdgeView
  Time Settings, System Information, and reboot system

## Slide 18: Lesson 2.2: Initial Configuration - Review
EdgeMarc Voice Operating System currently on version 14.x
Make sure you note the two “root” passwords
  GUI – “default”
  CLI – “(Hold the Shift Key and Type) 2345678109”
Accessing EdgeMarc remotely using SSH, HTTP, etc., requires that the Firewall settings be configured under the “Security” menu

## Slide 19: Lesson 2.2: Initial Configuration - Questions
What version of Embedded Linux is the basis for VOS?
Should you and your Linux Sys Admin colleagues “modify” VOS by adding scripts, additional services, maybe a really cool nginx web server?

## Slide 20: Lesson 2.3: Securing the Edgemarc
User Management & Setting passwords
  Root vs Admin user
  Changing Root default password for GUI & VOS CLI access
  Session, Password & Account configuration options
Firewall Traversal & restricting access to the management interface
Implementing Trusted Hosts
Overview of HTTPS implementation

## Slide 21: Lesson 2.3: Securing the Edgemarc - User Management
EdgeMarc can be configured with the following types of “users”
  The root user with GUI and CLI access
  System users with read or read/write GUI access, managed internally
  External Authentication Server (RADIUS or TACACS+) users
  FTP users – intended to be accounts so that devices such as Polycom IP Phones can use the EdgeMarc as an FTP provisioning server
Note that EdgeMarc users can only access the GUI or SSH from the LAN side unless Security / Firewall settings are modified to allow HTTP/HTTPS/SSH through the EdgeMarc Firewall.

## Slide 22: Lesson 2.3: User Management - Root vs Admin user
By default, only the root user can access the EdgeMarc GUI
As soon as User Management is enabled, EdgeMarc will create the user “admin” and require GUI login using the admin user, not the root user
Additional users can then be created

## Slide 23: Lesson 2.3: User Management - Default Password GUI & VOS CLI
When you start an EdgeMarc in default configuration, the user login account for the GUI and the CLI is:
  User name: root
  Password: default
Note that user Root has two distinct passwords:
  GUI password: “default”
  Command Line Interface Password: “(hold shift key and type) 2345678109”

## Slide 24: Lesson 2.3: Session, Password & Account configuration options
It may seem a bit awkward from a GUI perspective, but to “enable” user management in the EdgeMarc you must first enable “Session Management” (see Hands on Lab 3.1)
User Management can then be enabled and the “admin” user will automatically be created

## Slide 25: Lesson 2.3: Setting up Session and User Management

## Slide 26: Lesson 2.3: Session Management & Security
Accessing EdgeMarc from the WAN
Enabling Intrusion Detection. How does it work to protect the EdgeMarc?
Setting Basic WAN to LAN Firewall Traversal configuration for HTTP, HTTPS, TELNET, SSH, SNMP.
Configuring Trusted Hosts
Creating and / or adding a Certificate. What is a “Signed Certificate” and how do you obtain one?
Setting up HTTPS

## Slide 27: Lesson 2.3: Accessing EdgeMarc from the WAN
It is possible to login remotely via:
  HTTP/HTTPS GUI
  SSH
It is also possible to allow SNMP access from a remote server such as a Syslog Server / EdgeView
To access the EdgeMarc remotely, it is necessary to adjust the Firewall traversal settings under “Security”.

## Slide 28: Lesson 2.3: Enabling Intrusion Detection
The Intrusion Prevention page allows a user to set a number of unsuccessful login attempts a remote host may have during a period of time before that remote host is locked out from being able to attempt to login.
The user will be locked out from the time of the first unsuccessful login to the lockout duration.

## Slide 29: Lesson 2.3: Enabling Intrusion Detection
Once Enable Intrusion Detection is enabled, additional configuration options are displayed.

## Slide 30: Lesson 2.3: Firewall Traversal configuration
The main EdgeMarc Firewall Traversal feature allows you to set up a secure tunnel from a remote client to an external server. All traffic going through this tunnel is encrypted and will be explored in Module 4.0.
It is also important to consider the Security settings for the traversal of “management protocols” such as HTTP/HTTPS, FTP, SSH, & SNMP as a type of Firewall Traversal.

## Slide 31: Lesson 2.3: Firewall Traversal configuration

## Slide 32: Lesson 2.3: Configuring Trusted Hosts
The Trusted Hosts page defines a list of hosts or networks that are able to access the system using management protocols.
These management protocols are configured using the settings on the Basic WAN Firewall Settings page.
Choose Security from the Configuration Menu and refer to Configuring Basic WAN Firewall Settings.
Note that once a trusted address is defined, only hosts in the trusted list are allowed to access the system!

## Slide 33: Lesson 2.3: Configuring Trusted Hosts
Be Careful!
If you are accessing the EdgeMarc from the WAN side, be sure to add your IP address or subnet

## Slide 34: Lesson 2.3: Adding a Certificate
Certificates pre-installed on the system allow quick VoIP Traversal setup and testing.
These certificates ARE NOT secure for use in production
For production, generate new certificates
All certificates are kept in the Certificate list and can be downloaded

## Slide 35: Lesson 2.3: Adding a Certificate
The certificate list shows all certificates available on the system. The following certificate types are supported:
  HTTPS—Self-signed or generated by Certificate Authority (CA). Used for secure connections
  CA Certificate—Used to sign other certificates
  VoIP Traversal Server—Used by a VoIP Traversal server
  VoIP Traversal Client—Used by a VoIP Traversal client

## Slide 36: Lesson 2.3: Adding a Certificate
Note that creating a certificate may require a lot of CPU resources and should not be done while the system is in service.

## Slide 37: Lesson 2.3: Setting up HTTPS
The HTTPS Configuration page configures the certificate used by HTTPS for secure remote management as well as any alternate HTTPS port to use
Access to the system from the WAN or public interface requires HTTPS access, which is enabled on the Firewall page

## Slide 38: Module 2.0: Review
Various EdgeMarcs support different physical interfaces on the LAN & WAN side
Some EdgeMarcs include legacy PSTN interface such as T-1, ISDN, PRI and Analog trunks / station ports.
EdgeMarc includes a GUI for system admin & configuration
It is possible to Access EdgeMarc via the console RS-232 port or via SSH

## Slide 39: Module 2.0: Quiz
What version of VOS is running on your EdgeMarc?
What is THE root password?
After starting up an EdgeMarc from default configuration, is there a risk that a hacker could access it via SSH from a remote location?
What is SSH and what is Putty?