## Slide 1: Module 4.0
Advanced Topics

## Slide 2: Module 4.0: Performance Objectives
In this module, attendees follow pre-defined scripts to complete advanced EdgeMarc configuration. The emphasis is on completing pre-defined settings tasks and demos of functionality.

## Slide 3: Module 4.0: Hands On Labs
Lab 1: Demo & Settings for Advanced Topuics
Traffic Shaping – config settings
Firewall setup with Proxy Arp Demo
WAN Failover config & Demo
High Availability – Demo
VoIP Survivability – Config and Demo

## Slide 4: Module 4.0 Lessons
Lesson 1.0: Traffic Shaping
Lesson 2.0: Firewall Deployment
Lesson 3.0: WAN Failover
Lesson 4.0: High Availability
Lesson 5.0: VoIP Survivability

## Slide 5: Lesson 4.1: Traffic Shaping
Understanding QoS options
EdgeMarc LAN/WAN VoIP prioritization options

## Slide 6: Lesson 4.1: Traffic Shaping
Class based queues
  Voice & Signaling are high priority. Everything else is low priority.
  Traffic Scheduler to service the queues
  Traffic Shaper to rate limit low priority traffic
TOS / Diffserv packet marking on LAN and WAN.
  High-priority TOS value is re-written to 0xb8 (Diffserv AF46)
  Low-priority TOS value is re-written to 0x00
TCP congestion management
  TCP acknowledgements to WAN are delayed to push back on inbound data traffic
  Proved effective in field. Allows inbound voice to avoid high jitter

## Slide 7: Lesson 4.1: Traffic Shaping - Access Link
Single Device to Manage Bandwidth
and Improve Quality
Traffic shaping—dynamic voice prioritization
Call Admission Control—no oversubscription
Diffserv marking and policing
Up to 8 class of service queues
Voice
Data
T1 WAN Link
1.544 Mbps
VoIP calls established
Data “shaped”
New calls are blocked
Data not starved
completely
Data allowed to consume available bandwidth as calls are completed
High Priority Queue
Low Priority Queue
time
High Priority
Queue
Low Priority
Queue
WAN/LAN Link

## Slide 8: Lesson 4.1: Traffic Shaping – Bandwidth Management
Call Access Control (CAC)
Configure maximum allowed calls
Send “Bandwidth Exceeded” signaling message at call n+1 (inbound or outbound)
This value is configured in the VoIP ALG page
Working together with automatic classing, queuing and traffic shaping, CAC ensures the WAN link will not be over subscribed by having too many RTP streams requiring WAN access.

## Slide 9: Lesson 4.1: Traffic Shaping - Configuration
Enable the TS
Enter the real life Upstream and Downstream (from www.speakeasy.net for example). Configure the Secondary Interface only when WLR is ON
Enable the CAC (optional)
Enter the Max number of calls depending on the codec and the Bandwidth
Company Confidential

## Slide 10: Lesson 4.1: Traffic Shaping - Configuration
Enable Traffic shaping
Set up and down stream bandwidth based on a speed test.
80% of Average of 5 tests.
Notes: Enabling Traffic Shaping is required to deliver a business quality voice service over the IP network.
Best practice is to configure the Primary WAN downstream and upstream bandwidths to be 80% of the average of 5 speed tests performed on a “naked” circuit. These parameters must describe the circuit that was delivered, not the circuit that was sold!
Call admission control can be a very important part of delivering a business quality voice service. Best practice is to calculate the maximum number of calls supported on the link based on the expected mix of codecs. By setting the CAC you ensure that quality is maintained for calls in progress when the link has reached its capacity. New calls will be gracefully declined instead of degrade the quality of all calls in progress.
Configuration of the secondary wan link is beyond the scope of this presentation.

## Slide 11: Lesson 4.1: Traffic Shaping - Advanced - COS
Notes: Enabling Traffic Shaping is required to deliver a business quality voice service over the IP network.
Best practice is to configure the Primary WAN downstream and upstream bandwidths to be 80% of the average of 5 speed tests performed on a “naked” circuit. These parameters must describe the circuit that was delivered, not the circuit that was sold!
Call admission control can be a very important part of delivering a business quality voice service. Best practice is to calculate the maximum number of calls supported on the link based on the expected mix of codecs. By setting the CAC you ensure that quality is maintained for calls in progress when the link has reached its capacity. New calls will be gracefully declined instead of degrade the quality of all calls in progress.
Configuration of the secondary wan link is beyond the scope of this presentation.

## Slide 12: Lesson 4.1: Traffic Shaping - Advanced - Classification Rules
Notes: Enabling Traffic Shaping is required to deliver a business quality voice service over the IP network.
Best practice is to configure the Primary WAN downstream and upstream bandwidths to be 80% of the average of 5 speed tests performed on a “naked” circuit. These parameters must describe the circuit that was delivered, not the circuit that was sold!
Call admission control can be a very important part of delivering a business quality voice service. Best practice is to calculate the maximum number of calls supported on the link based on the expected mix of codecs. By setting the CAC you ensure that quality is maintained for calls in progress when the link has reached its capacity. New calls will be gracefully declined instead of degrade the quality of all calls in progress.
Configuration of the secondary wan link is beyond the scope of this presentation.

## Slide 13: Lesson 4.2: Firewall Traversal & Proxy ARP
Deployment models using Proxy ARP
Firewall Traversal settings

## Slide 14: Lesson 4.2: Firewall Traversal
Using EdgeMarc Firewall Traversal options
Internal Client, External Server, Remote Client

## Slide 15: Lesson 4.2: Firewall Traversal & Proxy ARP
Proxy Arp is used when you want to assign a LAN side device, a Public IP address, which is on the same subnet as the WAN IP address
In this example, the EdgeMarc WAN IP address is 66.134.240.114/255.255.255.0 with a default gateway of 66.134.240.1.
And customer wants 66.134.240.115 on the LAN side server.

## Slide 16: Lesson 4.2: Firewall Traversal & Proxy ARP

## Slide 17: Lesson 4.2: Firewall Traversal & Proxy ARP
When you ping the Proxied IP address from a remote computer. The incoming icmp request should contain a destination MAC address of the EdgeMarc eth1 interface. If the destination MAC address does not match eth1 MAC address, the upstream router needs to clear its ARP cache. If customer have cable modem, customer need to power cycle the cable modem.
Use tcpdump with option “e” to see the destination MAC address.

## Slide 18: Lesson 4.2: Firewall Traversal & Proxy ARP
# tcpdump -nei eth1 -s0 icmp
tcpdump: listening on eth1
01:34:29.937686 0:3:6d:f6:2c:b4 a8:70:a5:0:26:53 0800 75: 24.49.104.166 > 66.134.240.115: icmp: echo request

## Slide 19: Lesson 4.2: Firewall Traversal & Proxy ARP
# ifconfig eth1
eth1 Link encap:Ethernet HWaddr A8:70:A5:00:26:53
inet addr:66.134.240.114 Bcast:66.134.240.255 Mask:255.255.255.0
inet6 addr: fe80::aa70:a5ff:fe00:2653/64 Scope:Link
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
RX packets:139235 errors:0 dropped:0 overruns:0 frame:0
TX packets:799 errors:0 dropped:0 overruns:0 carrier:0
collisions:0 txqueuelen:1000
Base address:0x3600

## Slide 20: Lesson 4.3: WAN Link Redundancy
Understanding Voice & Data options for WAN fail over
Primary vs Secondary WAN links
Configuring WAN Failover using revertive mode

## Slide 21: Lesson 4.3: WAN Link Redundancy
IP WAN
IP Phone
L
A
N
EdgeMarc
Secondary
WAN Link
Primary
WAN Link

## Slide 22: Lesson 4.3: WAN Link Redundancy

## Slide 23: Lesson 4.3: WAN Link Redundancy

## Slide 24: Lesson 4.3: WAN Link Redundancy

## Slide 25: Lesson 4.4: High Availability
Configuring HA
IPv4 vs IPv6 configuration

## Slide 26: Lesson 4.4: High Availability
HA is designed to remove any single point of failure in the network configuration:
  Physical
  Data link
  Network routing
  ALG
    B2BUA is not HA compliant
  Hot failover
Company Confidential

## Slide 27: Lesson 4.4: High Availability Architecture
IP WAN
IP Phone
L
A
N
HA Pair

## Slide 28: Lesson 4.4: High Availability Architecture

## Slide 29: Lesson 4.4: High Availability - Configuration

## Slide 30: Lesson 4.4: High Availability - Configuration

## Slide 31: Lesson 4.4: High Availability – Configuration
List of interfaces
Enabling the maintenance mode
Enabling HA
Enabling a mode where when the primary EM is back up, it is becoming the master of the HA pair again automatically
Configuring the primary versus secondary EM
State full configuration
Configuring the Networking HA
Company Confidential

## Slide 32: Lesson 4.5: VoIP Survivability
Setting up redundant Softswitch / IP PBX configurations
WAN Link failure & local call control

## Slide 33: Lesson 4.5: VoIP Survivability
Survivability is a collection of features that enable the system to extend the availability of VoIP services.
These features include:
  Support for redundant Softswitches/IP PBX's
  Local call control in the event of WAN link failure, softswitch/IP PBX failure, or during periods of network congestion that result in loss of connectivity to a remote Softswitch/IP PBX

## Slide 34: Lesson 4.5: VoIP Survivability – Redundant SIP Server / IP PBX
WAN
IP PBX / SIP Server
IP PBX / SIP Server

## Slide 35: Lesson 4.5: VoIP Survivability
Local dial tone in case of network disruption:
  Station-to-station
  Hold
  Transfer
3-way conference
Outbound/Emergency calls with integrated gateway

## Slide 36: Lesson 4.5: VoIP Survivability - Features
Available for all EdgeMarc series appliances
Application layer monitoring of softswitch connectivity
Automatic failure detection and return of call control
Support for redundant softswitch servers
Automatic creation of local dial plan to simplify setup
Dial plan integration with Softswitch
Local call switching between SIP user agents and PSTN gateway
Transfer, hold and conference capability when in local mode (5300 adds voicemail)

## Slide 37: Lesson 4.5: VoIP Survivability – Deployment Examples
EdgeMarc can accommodate very complex survivability implementation architectures.
See the document in your student materials called “Application_Note-Configuring_Survivability_features”

## Slide 38: Lesson 4.5: VoIP Survivability – Basic Configuration
First step is create a list of SIP Servers that EdgeMarc can prioritize
Typically two SIP Servers
Can be manually added to SIP Settings or DNS SRV Record lookup can obtain list of SIP Servers

## Slide 39: Lesson 4.5: VoIP Survivability – Advanced Settings
Walk through the settings on the Survivability Page
Refer to the Application Note for use case and sample configuration settings

## Slide 40: Module 4.0: Review

## Slide 41: Module 4.0: Quiz