## Slide 1: Module 3.0
EdgeMarc LAN/WAN Basic Configuration

## Slide 2: Module 3.0: Performance Objectives
Gain experience with the core configuration of EdgeMarc & real world LAN/WAN deployments.
Understand the flexibility and range of EdgeMarc network functions.
Build EdgeMarc centered functional VoIP infrastructure.

## Slide 3: Module 3.0: Hands On Labs
Lab 1: Setting up Users & User Management
Lab 2: Session Management Configuration & Security
Lab 3: SSH, HTTP/HTTPS WAN Access & Security
Lab 4: Planning VLAN configuration for Voice & Data
Lab 5: Setting up EdgeMarc DHCP Server
Lab 6: Running EdgeMarc Network Test Tools

## Slide 4: Demos – VoIP Basics
Demo 1: Configure Asterisk/Elastix IP PBX – LAN
Demo 2: Troubleshooting SIP with Wireshark
Demo 3: Configuring Linux based FTP Provisioning Server to work with EdgeMarc DHCP Server
Demo 5: External Firewall deployment with EdgeMarc using Proxy ARP
Demo 6: Securing VoIP – Implementing SRTP & SIP/TLS

## Slide 5: Module 3.0: Lessons
Lesson 1.0: User Management, Session Management & WAN/LAN Firewall Traversal
Lesson 2.0: EdgeMarc LAN Configuration Details
Lesson 3.0 EdgeMarc WAN Configuration Details
Lesson 4.0 Advanced Topics in EdgeMarc LAN/WAN Configuration

## Slide 6: Lesson 3.1: User Mgt, Session Mgt & Firewall Traversal
User Management
Session Management & Security
MOTD settings

## Slide 7: Lesson 3.1-1: User Management
  Root vs Admin user
  Changing Root default password for GUI & VOS CLI access
  Session, Password & Account configuration options
  Setting up Session and User Management
  Introduction to RADIUS & TACACS+ Server configurations
  FTP User setup and management

## Slide 8: Lesson 3.1 User Management
EdgeMarc can be configured with the following types of “users”
  The root user with GUI and CLI access
  System users with read or read/write GUI access, managed internally
  External Authentication Server (RADIUS or TACACS+) users
  FTP users – intended to be accounts so that devices such as Polycom IP Phones can use the EdgeMarc as an FTP provisioning server
Note that EdgeMarc users can only access the GUI or SSH from the LAN side unless Security / Firewall settings are modified to allow HTTP/HTTPS/SSH through the EdgeMarc Firewall.

## Slide 9: Lesson 3.1-1.1: Root vs Admin user
By default, only the root user can access the EdgeMarc GUI
As soon as User Management is enabled, EdgeMarc will create the user “admin” and require GUI login using the admin user, not the root user
Additional users can then be created

## Slide 10: Lesson 3.1-1.2: default password for GUI & VOS CLI access
When you start an EdgeMarc in default configuration, the user login account for the GUI and the CLI is:
  User name: root
  Password: default
Note that user Root has two distinct passwords:
  GUI password: “default”
  Command Line Interface Password: “(hold shift key and type) 2345678109”

## Slide 11: Lesson 3.1-1.3: Session, Password & Account configuration options
It may seem a bit awkward from a GUI perspective, but to “enable” user management in the EdgeMarc you must first enable “Session Management” (see Hands on Lab 3.1)
User Management can then be enabled and the “admin” user will automatically be created

## Slide 12: Lesson 3.1-1.4: Setting up Session and User Management

## Slide 13: Lesson 3.1-1.5: RADIUS & TACACS+ Server configurations
EdgeMarc can work with a RADIUS or TACACS+ AAA Server for user authentication
If an external Authentication server is configured on the EdgeMarc, the internal users, include “admin” cannot login to the GUI, not even on the LAN!

## Slide 14: Lesson 3.1-1.5: RADIUS & TACACS+ Server configurations
WAN
FTP Provisioning Server
TACACS+ Server
IP PBX / SIP Server
RADIUS Server
Pick One… You can’t run both RADIUS & TACACS+ at the same time with EdgeMarc

## Slide 15: Lesson 3.1-1.5: RADIUS & TACACS+ Server configurations
WAN
TACACS+ Server
Once the EdgeMarc is configured to work with the Authentication Server it WILL NOT allow the internal user accounts to access the GUI, not even “admin”!

## Slide 16: Lesson 3.1-1.5: RADIUS & TACACS+ Server configurations

## Slide 17: Lesson 3.1-1.5: RADIUS & TACACS+ Server configurations

## Slide 18: Lesson 3.1-1.6: FTP User setup and management
FTP users are intended to be used when EdgeMarc is acting as an FTP provisioning server
A typical FTP user would be the default Polycom IP Phone account:
  user name: PlcmSpIp
  Password: PlcmSpIp

## Slide 19: Lesson 3.1-2: Session Management & Security
Accessing EdgeMarc from the WAN
Enabling Intrusion Detection. How does it work to protect the EdgeMarc?
Setting Basic WAN to LAN Firewall Traversal configuration for HTTP, HTTPS, TELNET, SSH, SNMP.
Configuring Trusted Hosts
Creating and / or adding a Certificate. What is a “Signed Certificate” and how do you obtain one?
Setting up HTTPS

## Slide 20: Lesson 3.1-2.1: Accessing EdgeMarc from the WAN
It is possible to login remotely via:
  HTTP/HTTPS GUI
  SSH
It is also possible to allow SNMP access from a remote server such as a Syslog Server / EdgeView
To access the EdgeMarc remotely, it is necessary to adjust the Firewall traversal settings under “Security”.

## Slide 21: Lesson 3.1-2.2: Enabling Intrusion Detection
The Intrusion Prevention page allows a user to set a number of unsuccessful login attempts a remote host may have during a period of time before that remote host is locked out from being able to attempt to login.
The user will be locked out from the time of the first unsuccessful login to the lockout duration.

## Slide 22: Lesson 3.1-2.2: Enabling Intrusion Detection
Once Enable Intrusion Detection is enabled, additional configuration options are displayed.

## Slide 23: Lesson 3.1-2.3: Firewall Traversal configuration
The main EdgeMarc Firewall Traversal feature allows you to set up a secure tunnel from a remote client to an external server. All traffic going through this tunnel is encrypted and will be explored in Module 4.0.
It is also important to consider the Security settings for the traversal of “management protocols” such as HTTP/HTTPS, FTP, SSH, & SNMP as a type of Firewall Traversal.

## Slide 24: Lesson 3.1-2.3: Firewall Traversal configuration

## Slide 25: Lesson 3.1-2.4: Configuring Trusted Hosts
The Trusted Hosts page defines a list of hosts or networks that are able to access the system using management protocols.
These management protocols are configured using the settings on the Basic WAN Firewall Settings page.
Choose Security from the Configuration Menu and refer to Configuring Basic WAN Firewall Settings.
Note that once a trusted address is defined, only hosts in the trusted list are allowed to access the system!

## Slide 26: Lesson 3.1-2.4: Configuring Trusted Hosts
Be Careful!
If you are accessing the EdgeMarc from the WAN side, be sure to add your IP address or subnet

## Slide 27: Lesson 3.1-2.5: Adding a Certificate
Certificates pre-installed on the system allow quick VoIP Traversal setup and testing.
These certificates ARE NOT secure for use in production
For production, generate new certificates
All certificates are kept in the Certificate list and can be downloaded

## Slide 28: Lesson 3.1-2.5: Adding a Certificate
The certificate list shows all certificates available on the system. The following certificate types are supported:
  HTTPS—Self-signed or generated by Certificate Authority (CA). Used for secure connections
  CA Certificate—Used to sign other certificates
  VoIP Traversal Server—Used by a VoIP Traversal server
  VoIP Traversal Client—Used by a VoIP Traversal client

## Slide 29: Lesson 3.1-2.5: Adding a Certificate
Note that creating a certificate may require a lot of CPU resources and should not be done while the system is in service.

## Slide 30: Lesson 3.1-2.6: Setting up HTTPS
The HTTPS Configuration page configures the certificate used by HTTPS for secure remote management as well as any alternate HTTPS port to use
Access to the system from the WAN or public interface requires HTTPS access, which is enabled on the Firewall page

## Slide 31: Lesson 3.1-3: MOTD Settings
The following message types are supported:
System Authorization Message of the Day
HTTP/HTTPS Short System Authorization Message of the Day
System Greeting Message of the Day

## Slide 32: Lesson 3.1: User Mgt, Session Mgt & Firewall Traversal - Review
EdgeMarc supports a series of users, beginning with the core system users “root” and admin
External Authentication Servers (RADIUS or TACACS+) may be configured
FTP users are intended for specific tasks such as IP Phone provisioning
EdgeMarc includes a very sophisticated Firewall and intrusion detection functionality
Secure access to EdgeMarc such as using HTTPS requires a Certificate
MOTD can be configured by admin and displayed to users as they login

## Slide 33: Lesson 3.1: User Mgt, Session Mgt & Firewall Traversal - Questions
List the types of EdgeMarc users.
If an external TACACS+ server is configured to work with an EdgeMarc, can the admin user still login to EdgeMarc on the LAN side. Explain your answer.
Is it necessary to enable SSH and SNMP access through the Firewall to an EdgeMarc? What are the advantages and disadvantages for “Network Edge Orchestration”?

## Slide 34: Lesson 3.2: EdgeMarc LAN Configuration Details
Reviewing the Main Network GUI Page
Defining IPv4 & IPv6 DHCP requirements
NAT Configuration
Network Information & Testing Options
Ethernet / Layer 2 LAN/WAN Configuration

## Slide 35: Lesson 3.2-1: Main Network GUI Page
  The main network page allows for the configuration of the EdgeMarc LAN & WAN sides
  Note that EdgeMarc offers extensive IPv6 support
  VLAN may be enabled on the LAN and/or WAN side

## Slide 36: Lesson 3.2-2: IPv4 & IPv6 DHCP requirements
The EdgeMarc 4700 default configuration includes an enabled DHCP server.
The EdgeMarc internal LAN interface is assigned IPv4 address 192.168.1.1/24.
Connecting DHCP clients receive addresses starting with 192.168.1.100/24.
The EdgeMarc DHCP server can be configured to assign addresses from any range. The built in DHCP server includes the ability to configure all the key DHCP “Options”.

## Slide 37: Lesson 3.2-2: IPv4 & IPv6 DHCP requirements
Options are used to inform connecting clients about associated network services such as the IP address or FQDN (Fully Qualified Domain Name) of important support servers.
For example, when setting up the EdgeMarc DHCP server, the address of an FTP (File Transfer Protocol) or TFTP (Trivial FTP) Server can be included.
EdgeMarc also supports the very useful “Option 129” VLAN Discovery.

## Slide 38: Lesson 3.2-3: NAT Configuration
  How NAT functions
  When to apply Port Forwarding Rules
  Configuring a Private Network

## Slide 39: Lesson 3.2-3: NAT Configuration
NAT is only supported in IPv4
NAT Traversal is a constant problem for VoIP
EdgeMarc implements ALG/B2BUA to map the common public address to unique private addresses so internal IP Phones can accept incoming VoIP calls (a very nice feature!)

## Slide 40: Lesson 3.2-4: Network Information & Testing Options
  Display & review Network Information
  Run Network Tests; Ping & Traceroute
  Performing a network restart using the GUI option

## Slide 41: Lesson 3.2-5: Ethernet / Layer 2 LAN/WAN Configuration
  Using the Switch Ports
    View Link rate details
    Understand the advantages & disadvantages of adjusting link rate settings
  VLAN configuration support in the EdgeMarc
  Why is VLAN important in VoIP deployments?
  Enabling VLAN in LAN settings on the main Network GUI page
  VLAN membership & physical LAN ports
  Configuring IP Phones & other LAN devices to utilize VLAN settings
  802.1X Supplicant
    Understanding how 802.1X Authentication works
    Deployment examples
    Using EAP with RADIUS Server

## Slide 42: Lesson 3.2-5: Ethernet / Layer 2 LAN/WAN Configuration
Enable VLANS by checking this check box!

## Slide 43: Lesson 3.2-5: Ethernet / Layer 2 LAN/WAN Configuration
Notes: VLANs are not required to provide business quality voice service. If you do choose to use them, then you will configure them on this page.
Please note that port 4 is statically assigned to the first VLAN defined on the EdgeMarc. That is why we recommend configuring from LAN port 4, so you do not loose connectivity to the EdgeMarc when you turn on VLANs.
Each VLAN port can support:
  802.1 - traffic is untagged and the port is statically assigned to a configurable VLAN. The downstream device does not have to be VLAN capable.
  802.1q - traffic is tagged and multiple VLANs are present on the port. The downstream device must also be 802.1q capable.

## Slide 44: Lesson 3.2-5: Ethernet / Layer 2 LAN/WAN Configuration

## Slide 45: Lesson 3.2-5: Ethernet / Layer 2 LAN/WAN Configuration

## Slide 46: Lesson 3.2: EdgeMarc LAN Configuration Details - Review
EdgeMarc supports core LAN configuration options, including:
  A robust DHCP Server
  Full featured IPv4 NAT capabilities
  VLAN configuration options

## Slide 47: Lesson 3.2: EdgeMarc LAN Configuration Details - Questions
Why is NAT only supported in IPv4?
Why is VLAN commonly used with VoIP equipment?
What is DHCP Option 66?
What is the name of the actual standard for VLAN?

## Slide 48: Lesson 3.3: EdgeMarc WAN Configuration Details
WAN Settings on Main Network GUI Page
Switch Port settings for WAN Ethernet interface
WAN VLAN configuration
Setting up Static Routes
WAN Failover Introduction

## Slide 49: Lesson 3.3-1: WAN Settings on Main Network GUI Page
  Setting IPv4 & IPv6 WAN Interface options
  DNS Server settings
  Setting a Network Default Gateway

## Slide 50: Lesson 3.3-1: Main Network GUI Page – WAN Settings
The WAN interface may be set to Static IPv4 Address or act as a DHCP client
EdgeMarc also supports VLAN configuration for the WAN side

## Slide 51: Lesson 3.3-3: WAN VLAN configuration
WAN VLAN is configured when required by the WAN service provider
Enabled on the main Network page
Use the WAN VLAN Configuration page to configure the system WAN Ethernet port to support tagged VLANs
By default, all traffic (including data and voice) is tagged with VLAN ID 1

## Slide 52: Lesson 3.3-3: WAN VLAN configuration

## Slide 53: Lesson 3.3-4: Setting up Static Routes
Static routes may be needed to support network applications (such as a web server) that are allowed through the firewall and directed to a specific IP address or subnet
Use with Caution!
Static routes may prevent the other networking features in the system from functioning properly

## Slide 54: Lesson 3.3: Review

## Slide 55: Lesson 3.3: QQ&A – Quizzes, Questions, & Answers!

## Slide 56: Lesson 3.4 Advanced Topics in EdgeMarc Configuration
Configuration examples using Proxy ARP
Firewall Pass Through Rules & Sub Interfaces

## Slide 57: Lesson 3.4-1: Configuration examples using Proxy ARP
  Why use Proxy ARP?
  Flushing ARP caches

## Slide 58: Lesson 3.4-1: Configuration examples using Proxy ARP
Proxy using the Address Resolution Protocol to create a bridge between two interfaces on the system.
Proxy ARP is used when you want to assign a LAN side device (e.g. Firewall), a Public IP address, which is on the same subnet as the WAN IP address.
If you are trying to forward a separate (second) subnet to the LAN side on the EdgeMarc which is not in the same subnet as the WAN IP of the EdgeMarc, use Sub Interface and Forwarding Rules (in the GUI).
Note: Flush the upstream router ARP cache after configuring Proxy ARP so that the upstream router can re-associate the “proxyed" IP address with this system WAN MAC address.

## Slide 59: Lesson 3.4-1: Configuration examples using Proxy ARP
Fire Wall
EdgeMarc
IP WAN
L
A
N

## Slide 60: Lesson 3.4-1: Configuration examples using Proxy ARP
Firewall
EdgeMarc
IP WAN
L
A
N
Firewall is assigned
66.134.240.115/255.255.255.0
EdgeMarc is assigned
66.134.240.114/255.255.255.0
Default route 66.134.240.1
For both the EdgeMarc and the Firewall

## Slide 61: Lesson 3.4-1: Configuration examples using Proxy ARP
When configuring Proxy ARP, the upstream router will need to associate the proxied IP address with this system's WAN MAC address. Flush the upstream router's ARP cache after configuring Proxy ARP.
66.134.240.115
32
66.134.240.1
32 bit mask for a single IP Address

## Slide 62: Lesson 3.4-1: Configuration examples using Proxy ARP
Ping the Proxied IP address from a remote computer
Incoming icmp request should contain a destination MAC address of the EdgeMarc eth1 interface
If the destination MAC address does not match eth1 MAC address, the upstream router needs to clear its ARP cache. If customer have cable modem, customer need to power cycle the cable modem.
Use tcpdump with option “e” to see the destination MAC address.
# tcpdump -nei eth1 -s0 icmp
tcpdump: listening on eth1
01:34:29.937686 0:3:6d:f6:2c:b4 a8:70:a5:0:26:53 0800 75: 24.49.104.166 > 66.134.240.115: icmp: echo request
# ifconfig eth1
eth1 Link encap:Ethernet HWaddr A8:70:A5:00:26:53
inet addr:66.134.240.114 Bcast:66.134.240.255 Mask:255.255.255.0
inet6 addr: fe80::aa70:a5ff:fe00:2653/64 Scope:Link
UP BROADCAST RUNNING MULTICAST MTU:1500 Metric:1
Toubleshooting Proxy ARP

## Slide 63: Lesson 3.4-2: Firewall Pass Through Rules & Sub Interfaces
  Why do we need Pass Through?
  Pass Thru vs NAT Port Forwarding
  What is a Sub-Interface?
  Combining sub-interfaces with firewall pass through rules

## Slide 64: Lesson 3.4-2: Firewall Pass Through Rules & Sub Interfaces
Pass-Through Rules allow you to forward data traffic for a subnet from one interface to another, overriding the firewall default drop rules
Subnet forwarding is commonly used when servers with public addresses are placed behind the system. Configuring the network in this way allows the system to manage and prioritize bandwidth, sharing it between the VoIP services and the servers.
The subnet and pass-through addresses are not protected by the firewall.

## Slide 65: Lesson 3.4-2: Firewall Pass Through Rules & Sub Interfaces

## Slide 66: Lesson 3.4-2: Firewall Pass Through Rules & Sub Interfaces
A common use for subinterfaces is forwarding a public subnet. A subinterface may be created to support a subnet forwarded through the system.
When forwarding a subnet through the system, it is necessary to assign an address for the subnet to act as the system subnet gateway.
To configure forwarding rules, choose Network > NAT > Port Forwarding and refer to Configuring Port Forwarding.

## Slide 67: Lesson 3.4-2: Firewall Pass Through Rules & Sub Interfaces

## Slide 68: Lesson 3.4: Firewall Pass Through Rules & Sub Interfaces - Review
Proxy ARP, Firewall Pass Through, and sub-interfaces are advanced topics in network configuration
EdgeMarc incorporates these and many other complex functions to support client VoIP deployments

## Slide 69: Lesson 3.4: Firewall Pass Through Rules/ Subinterfaces - Questions

## Slide 70: Module 3.0: Review
EdgeMarc User management includes the ability to create system users and authenticate locally, or integrate with an enterprise TACACS+/RADIUS server
EdgeMarc includes a sophisticated DHCP server that can provide excellent support for LAN based VoIP equipment
VLAN support includes both LAN and WAN VLAN configuration options
EdgeMarc includes advanced network configuration options such as Proxy ARP and Sub Interfaces